## Specifications Yamaha T-560
Type: Mono/Stereo Tuner
Tuning Bands: FM, MW
Tuning Scale: Analogue
FM Tuning Range: 87.6 to 108 MHz
MW Tuning Range: 525 to 1605 kHz
Sensitivity: 1.9uV (FM), 10uV (MW)
Signal to Noise Ratio: 84dB (FM), 55dB (MW)
Distortion: 0.1% (FM), 0.3% (MW)
Selectivity: 27dB (MW)
Frequency response: 30Hz to 15kHz (FM)
Output: 500mV (FM), 180mV (MW)
Semiconductors: 19 x transistors, 6 x IC, 1 x FET, 10 x LED, 17 x diodes
Dimensions: 435 x 92 x 305mm
Weight: 3.7kg
Year: 1981

Sensitivity

FM mono (1kHz@40kHz deviation on a 98MHz carrier)
1.2µV (-105.4dBm)
26dB S/N (5% THD)

FM stereo (1kHz@40kHz deviation on a 98MHz carrier)
40µV (-75 dBm)
46dB S/N (0.5% THD)

Best obtainable THD+N
0.05%

AM (1kHz@50% modulation on a 1MHz carrier)
15µV (-83.5dBm)

Test scale accuracy